## Slide 1: Adventitial Tissue Analysis in Coronary Atherosclerosis ATACA
Group 23
Sabrina Figueroa-Buezo, Adriana Guetter, Wei (Harrison) Li, Salil Patel, Daibo Zhang
Dr. Geert Schmid-Schönbein
Dr. Elliot McVeigh

## Slide 2: Background: Atherosclerosis Disease
Results from plaque build-up in the coronary arteries of the heart.
9.2 Million people/year are affected.
Easy to diagnose lesion types are:
  -fat
  -calcified
  -thrombotic
Clinically silent
Clinically silent or overt
Thickenning
(smooth muscle)
Macrophages
Lipid pools
Lipid core
Lipid core (Fibroatheroma)
Fibroatheroma + Calcium
Fibroatheroma +
Thrombosis
Notes: Atherosclerosis is a disease that contributes to 1 of every 3 deaths in the U.S and it can lead to a multitude of potentially life-threatening conditions. This progressive disease arises due to the formation of plaques composed of calcium, cholesterol, fatty materials, cell debris, and fibrous tissue on the inner walls of the vascular system. The majority of plaque deposits occur in the arteries, although lesions could also occur in the veins.
Atherosclerosis initiation is characterized by the thickening of the intimal layer of arteries as and accumulation of fat, shown in the diagram under I and type II.
The accumulation of fat progresses to atheroma, where the growth of plaque disrupts blood flow and causes shear stress in the vessels and eventually vascular wall damage. The disease might progress into forming a calcification and even rupture and become a thrombotic lesion as shown at the bottom of the diagram.
Considering the mechanism of plaque initiation, atherosclerosis can best be described as an inflammatory and progressive process that is strongly linked to lipid oxidation,16 as well as diseases including diabetes and high blood pressure.

## Slide 3: Background: Calcium Lesions
Clinical
Indicator of coronary artery disease.
Diagnosis possible by different imaging modalities.
Prognosis of atherosclerotic patients
Non-clinical
Theories of Etiology of Atherosclerosis
Morphological study of atherosclerotic lesions
Trends/patterns in Atherosclerotic patients
Pericardium
Epicardial Fat
Epicardium
Fat/ Connective Tissue
Calcified Lesion
Coronary Vessel + Adventitial Tissue
Notes: A great indicator for atherosclerosis diagnosis and prognosis is coronary artery calcium.
Currently, CAC formation is understood as an active biological process with systematic and coordinated cellular actions instead of the passive deposition of calcium.
Studies of the biochemical composition of CAC plaques have uncovered the involvement of calcification-related and are specultated to be a protective mechanism initiated by injured vascular cells to stabilize plaques and prevent progression of the disease. This speculation requires researchers to identify the surrounding tissue of these lesions also known as the epicardium. The epicardium might contain a percentage of fat which would support this theory. As more fat correlates with an autoimmune response which might lead to calcified lesions.
For this reason, understanding the geometry and morphological features of the coronary vessels with caclcified atherosclerotic lesions, fat lesions, and healthy vessels becomes essential when diving into the research of the etiology of the disease.

## Slide 4: Problem Statement
The etiology of atherosclerosis is controversial:
  Genetics
  Viruses, bacteria
  Fluid shear stress & arterial bifurcations.
  Inflammation and cholesterol related to diet
Progression of atherosclerotic lesions
Morphology of atherosclerosis
  Adventitial tissue in atherosclerotic lesions
Current pathological and imaging studies of atherosclerosis in humans omit critical anatomical information of surrounding tissue that can shed light on the initiation of atherosclerosis.
Notes: However, the etiology is still uncertain, especially with respect to the specific location of early lesions in arteries and how these lesions progress. Moreover, the relationship between calcified lesions and adventitial tissue is sought to study the morphology and the origin of atherosclerosis.
The problem of unresolved etiology and morphology is a result of technical limitations in investigating early lesions. Only very recently, calcium deposits, an early sign of atherosclerosis, have been identified. As such, many studies regarding the pathogenesis of atherosclerosis use tissue biopsies and images of arteries with advanced atherosclerosis, which result in difficulties in studying the early-stage development of the disease.
This limitation is due to the lack of tools available for processing, analyzing and quantifying available data in imaging scans to address early lesions.

## Slide 5: Current Technology: Non-Invasive Techniques
Imaging Modality | Coronary Angiography | CMR | CT-Scan | PET-Scan
Calcium | xx | x | xxx | x
Plaque Area | xxx | x | xx | x
Coronary vessel Anatomy | x | xx | xxx | -
Figure 1. Original CT-Scan obtained from Dr. E. McVeigh
Prakash, V. (2018). Computed Tomography Coronary Calcium Score and Coronary Angiography.
Chen. N, et. Al (2014). Resonance Imaging of the Coronary Sinus. Insights into Imaging
Jason M (2017). Detection of Atherosclerotic Inflammation
Chandy E. (2018). Systemic Involvement in ACS: Using CMR to study aortic wall.
Notes: The imaging methods to diagnose atherosclerotic patients and study the disease include the ones shown in the following table. All of these methods have limitations and some might be better than others in particular cases.
For our design, we were lucky enough to have the opportunity to work with CT-Scans given that they provided a reasonable image resolution with all of the features to study the morphology of atherosclerotic lesions and vascularity in the heart.
A CT scan machine is able to combine a series of X-ray images taken from different angles around your body and use computer processing to create cross-sectional images of the blood vessels and any soft tissues inside your body, these cross sections are commonly called slices. CT scan images are able to provide more detail than an X-ray scan.
However, CT imaging still has two main issues that limit its clinical use in direct atherosclerotic monitoring: (1) radiation exposure and (2) plaque progression and patient prognosis do not correlate well with the information on plaques that could be obtained from a CT scan. This is due to the fact that mild plaque might not appear on a CT-Scan.

## Slide 6: Objective & Goals for the Design
Goal : analyze tissues surrounding the coronary artery to help researchers verify theories about the etiology of atherosclerosis.
Main Objective: create a CT-scan processing tool for research and clinical studies of atherosclerotic lesions.
Objectives:
Reduce the need for human analysis of these images.
Provide the means for understanding adventitial tissue around atherosclerotic lesions.
Reduce the time for manual processing of CT-Scans when analyzing vessels.
Quantify adventitial tissue in a region of interest of the whole image.

## Slide 7: Our Design: Innovative Tool for Analysis
Characterize Surrounding Tissue
by Pixel Brightness
Determine
Centers of
Masses of
Different
Tissue
Output
Geometric
Distances
Linearize Vessel
Segment vessel of interest

## Slide 8
Import the CT image DICOM file into MATLAB as an indexed 3D Matrix <x,y,z>
Import the segmented vessel into MATLAB, parameterize its centerline to linearize the vessel.
Categorize the tissues surrounding the vessel and colorcode them based on type (e.g. fat, muscle)
Visualize the linearized vessel with surrounding tissues color coded by type
Extract the linearized vessel and its surrounding tissues from the CT image
Analyze the geometry of the tissues surrounding the vessel with length measurements and center of mass locations
Analyze the distribution of different types of tissues surrounding the vessel
Pre-processing
Data conditioning
Data parsing
Analysis
ITK-SNAP
MATLAB
MATLAB
MATLAB
Segment a section of the coronary artery using ITK-SNAP and store the output in an niFTI files.
Look for stenosis in coronary CT image

## Slide 9: Vessel Segmentation in ITK-SNAP
Pre
processing
ITK-SNAP
Select Region of Interest
Threshold Intensities to Capture
Insert Seeds in Vessel to Capture
Z slices
Contour Evolution

## Slide 10: Vessel Linearization
Pre
processing
MATLAB
Motivation:
Normalize segmented vessel
  Allows different vessels to be compared to each other
  Diminishes effects of differences between vessels such as curvature
Allows for a more intuitive way to view the progression of the vessel
Optimize computing efficiency
  Reduces size of region of interest
Process:
Normal Plane Calculation
Centerline Extraction
Tangent Vector Estimation

## Slide 11: Vessel Linearization (Centerline Extraction)
Pre
processing
MATLAB
Obtain centerpoints along segmented vessel
Presents centerpoints and visual “Skeleton” of the segmented vessel
Some centerpoints may be bad and will have to be manually deleted
Code developed by Zhennong Chen, a member of Dr. McVeigh’s lab
Centerline Extraction of “Right Coronary to Marginal Branch” segmented vessel

## Slide 12: Vessel Linearization (Tangent Vector Estimation)
Pre
processing
MATLAB
Fit a Parametrized Curve c(t) for each Centerpoint
  Define “Principal Direction” of vessel as “the direction (x,y,z) in which the vessel progresses the most”
  Fit 2 polynomials (degree decided by user), where each “Dependent” coordinate is a function of the “Principle Direction” coordinate
  Curve is fit with n points before and after centerpoint (total # of points = 2n+1)
Take Derivatives of Parametrized Curves and Evaluate Derivatives at Centerpoint
  The resulting vectors are the estimated tangent vectors ( )
General Case in 3D:

## Slide 13: Vessel Linearization (Tangent Vector Estimation)
Pre
processing
MATLAB
Fit a Parametrized Curve c(t) for each Centerpoint
  Define “Principal Direction” of vessel as “the direction (x,y,z) in which the vessel progresses the most”
  Fit 2 polynomials (degree decided by user), where each “Dependent” coordinate is a function of the “Principle Direction” coordinate
  Curve is fit with n points before and after centerpoint (total # of points = 2n+1)
Take Derivatives of Parametrized Curves and Evaluate Derivatives at Centerpoint
  The resulting vectors are the estimated tangent vectors ( )
2D Example where “Principal Direction” is in x direction (t = x):

## Slide 14: Vessel Linearization (Tangent Vector Estimation)
Pre
processing
MATLAB

## Slide 15: Vessel Linearization (Normal Plane Calculation)
Pre
processing
MATLAB
Estimated Tangent Vectors are Actually Normal Vectors for our Normal Planes
Planes will be 31x31 pixels (~10.5x10.5 mm)
Calculate Coordinates for Normal Plane using the following equation:
Where &
Stack Individual Normal Planes to obtain Linearized Vessel
A set to (0, 0, 0) in this drawing

## Slide 16: Vessel Linearization (Normal Plane Calculation)
Pre
processing
MATLAB
Estimated Tangent Vectors are Actually Normal Vectors for our Normal Planes
Planes will be 31x31 pixels (~10.5x10.5 mm)
Calculate Coordinates for Normal Plane using the following equation:
Where &
Stack Individual Normal Planes to obtain Linearized Vessel
We can think of each Normal Plane as a slice of bread. The Linearized Vessel would then be a loaf of bread.

## Slide 17: Vessel Linearization
Pre
processing
MATLAB
Nonlinearized Vessel
Linearized Vessel

## Slide 18: Tissue Characterization
Motivation:
Quantitatively characterize different tissues using pixel brightness in Hounsfield Units (HU)
Present results in a visual manner
MATLAB Tools for Colored Visualization of an Image:
ColorMaps
  Assigns specific colors to specific numerical values
  Many ColorMaps are already built into MATLAB
Labels
  Assigns Numerical Labels to specific numerical values
  Labels can be used for quantitative downstream analysis
processing
MATLAB
Tissue Type | HU Range | ColorMap Color | Numerical Label
Blood (Contrast Agent) | 650 to 985 | Red | 1
Vessel Lining | 277 to 600 | Blue | 2
Myocardium | -70 to 10 | Yellow | 3
Epicardial Fat | -148 to -70 | Purple | 4
Calcium | 1000+ | Green | 5

## Slide 19: Tissue Characterization (ColorMap)
Red - Blood (Contrast Agent)
Blue - Vessel Lining
Yellow - Myocardium
Purple - Epicardial Fat
Green - Calcium
processing
MATLAB
Linearized Vessel With Gray ColorMap
Linearized Vessel With Custom
ColorMap

## Slide 20: Tissue Characterization (Label)
processing
MATLAB

## Slide 21: Probability Distribution Analysis
processing
MATLAB
1
2
3
Pick slices of linearized vessel
Identify vessel
Identify tissue type outside vessel
Identify Calcium
Obtain % Distribution of tissue type around the vessel based on pixel distinction.
Muscle
Vessel
Calcium
Fat
pix.count/totalpix.
Label | %
Calcium | 0.092
Vessel Lining | 0.09
Epicardium | 40.587
Epicardial Fat | 35.527
Connective Tissue | 23.612

## Slide 22: Center of Mass
processing
MATLAB
Based off ct_label function: to create a binary matrix for each tissue type.
Formula for Binary Center of Mass: Mean value across x,y,z coordinates.
Goes across all x,y,z positions in the 3D Matrix
Label | X | Y | Z
Calcium | 9.6923 | 4.3654 | 43
Vessel Lining | 9.6154 | 10.731 | 18.346
Epicardium | 9.684 | 11.238 | 40.112
Epicardial Fat | 12.533 | 11.279 | 30.101
Label from Calcium | Min Distance | Max Distance
Vessel Lining | 8.8239 mm | 35.5839
Epicardium | 4.3050 mm | 57.7569
Epicardial Fat | 1.431 mm | 57.1848
Center of Mass Calcium
Distance to surrounding tissues
Across all z-slices
<x, y, z>
Ca lesion
Vessel Lining
Epicardial Fat
Epicardium

## Slide 23: Design Re-cap: Features
Linearize Vessels
Identify Tissue Types in each layer
Visualize in 3D different tissues and calcium
Extract 3D location of centroid of each tissue type and calcium
Extract Vessel
ITK-SNAP
MATLAB
Calculate Distribution of tissue around vessels with and without calcium
Calculate max. & min. Projected distance from lesion to different tissues

## Slide 24: Quantifying Analysis
Possible new frontier of cardiovascular research
Distance Measurements
Center of Mass Locations
Distribution of Tissue
E.g. shortest distance between lesion and fat tissue
Discover possible links between atherosclerosis and the transport of external pathological agent
E.g. relative location of different types of tissue More detailed investigation of the sites specificity of atherosclerosis
E.g. relative location of different types of tissue
Discover correlations between atherosclerosis and the tissue surrounding the vessel

## Slide 25: Results and Discussion
1. Robust integration between ITK-SNAP and MATLAB
Overlaying ITK-SNAP output with CT image recovers vessel location
The two platforms integrates well

## Slide 26: Results and Discussion
2. Adequately accurate centerline parameterization
3rd degree polynomials fitted to every 7 consecutive center points
Normalized Standard Error:
  4 • Standard Error / Vessel Diameter
  4 • Standard Error = 95% prediction interval
Opportunities for improvement:
  Centerline extraction accuracy
  Optimize fitting protocol

## Slide 27: Results and Discussion
3. A limitation of vessel linearization resolved
A major caveat of vessel linearization: bifurcated vessel cannot be linearized
  Branches of a bifurcated vessel segmented and linearized separately
However, informations regarding the bifurcation is not lost
  Captured with other tissues in the normal planes of the vessel

## Slide 28: Results and Discussion
4. Tissue characterization may need further testing and optimization
Verified with visual inspection
  Qualitative
  Time consuming
  Inaccurate
Further testing: Verify current tissue characterization results against expert recommendations
  Quantified statistical analysis

## Slide 29: Ethical Considerations
Patient Confidentiality
Patient consent to research use
De-identified Images
Patient information not required or inferred
Using phantoms for future testing

## Slide 30: Conclusions
Further understanding of atherosclerosis requires an analysis of tissue surrounding the coronary artery
We constructed a pipeline that lays the foundation for such studies
  Vessel linearization and tissue characterization
The pipeline attains a proof of concept
  Vessel linearization algorithms are proven acceptable robust
  Linearized vessels can be more intuitively visualized and analyzed
  Possibilities for tissue analysis is immense
More effort is required before the pipeline is ready for deployment
  More systematic analysis packages
  More intelligent tissue characterization techniques
  Better user experience and higher throughput

## Slide 31: Future Directions
Next Few Month
Next Year
Eventual Goal
Further test the pipeline with additional vessels from different images
Better integrate different components of the pipeline
Improve tissue analysis modules
Documentation
Improve user interface design and user experience
Adding more tissue analysis modules
Beta testing
Begin physiologically relevant studies with additional images
Improve the throughput of the pipeline (automation and software engineering)
Continue physiologically relevant studies with a large number of images
Generate new insights into the pathology of atherosclerosis

## Slide 32: Acknowledgements
For their technical guidance
  Dr. Geert Schmid-Schönbein
  Dr. Elliot McVeigh
  Zhennong Chen
For their professional support
  Neha Chhugani
  Dr. Bruce Wheeler

## Slide 33: THANK YOU! ANY QUESTIONS?